## Slide 1: 数字音频基础 Basics of Digital Audio

## Slide 2: Outline of Lecture 05
Digitization of Sound
  Sound and Digitization
  Nyquist Theorem
  Signal to Noise Ratio (SNR)
Quantization and Transmission of Audio
Experiments

## Slide 3: Sound and Digitization
What is Sound?
  Sound （声音）is a wave phenomenon like light, but is macroscopic and involves molecules of air being compressed and expanded under the action of some physical device.
  Sound is a pressure wave that moves through a compressible (可压缩的) medium
Characteristics of sound
  Amplitude （振幅）
    Measure the pressure at a location using voltage levels（电平）
  Frequency
    The number of periodic vibrations (震动) within a second

## Slide 4: Sound and Digitization
What is Sound?
  Frequency ranges of human and animals.

## Slide 5
Audio （音频）is the sounds human can hear
Frequency response
  20Hz-20kHz for human hearing
  Human are more sensitive to low frequencies
Speech （语音）is the sounds human can utter （说出）
  85HZ to 1,100HZ
  A human adjusts himself/herself very efficiently to different speakers and their speech habits
Sound and Digitization
Notes: 高于20KHz叫做超声

## Slide 6: Sound and Digitization
The signal is digitized in each dimension: in time and in amplitude
Sampling
  Convert continuous time into discrete time domain
  Typical sampling rate of audio: 8KHZ ~ 48KHZ
Quantization
  Convert continuous sample values into discrete values

## Slide 7: Sound and Digitization
Digitization
  Thus to decide how to digitize audio data we need to answer the following questions:
  What is the sampling rate?
  How finely is the data to be quantized, and is quantization uniform?
  How is audio data formatted? (file format)

## Slide 8: Nyquist Theorem
Complex signal by superposing sinusoids

## Slide 9: Nyquist Theorem
Signals can be decomposed into a sum of sinusoids.
  Whereas frequency is an absolute measure, pitch(音高/音调) is generally relative - a perceptual subjective quality of sound.
  Fourier transformation: Extract information of each components
https://zhuanlan.zhihu.com/p/19763358

## Slide 10: Nyquist Theorem
Nyquist Theorem（奈奎斯特理论）
  The Nyquist theorem states how frequently we must sample in time to be able to recover the original sound.

## Slide 11: Nyquist Theorem
Nyquist Theorem
  For correct sampling we must use a sampling rate equal to at least twice the maximum frequency content in the signal. This rate is called the Nyquist rate(奈奎斯特采样率).
  Nyquist frequency(奈奎斯特频率): half of the Nyquist rate.
  The relationship among the Sampling Frequency, True Frequency, and the Alias Frequency （假频） is as follows:
  , for

## Slide 12: Nyquist Theorem
思考题
如一个声音的频率为22.05kHz，
  奈奎斯特采样率应该为多少？
  44.1kHz
  如果采样频率为33.075kHz，则假频为多少？
  假频的计算公式为f假频=f采样频率-f真实频率，因此其假频为11.025kHz.

## Slide 13: Signal to Noise Ratio (SNR)
The ratio of the power of the correct signal and the noise is called the signal to noise ratio (SNR)
  A measure of the quality of the signal
  The SNR is usually measured in decibels (dB:分贝), where 1 dB is a tenth of a bel (贝尔)
  The SNR value, in units of dB, is defined in terms of base 10 logarithms of squared voltages, as follows:
SNR = 10log10(v2signal /v2noise) = 20log10(vsignal /vnoise)
To know: Power — 10; Signal Voltage — 20

## Slide 14: Signal to Noise Ratio (SNR)
Magnitude （量级） Range of Audio
  The levels of audio are described in terms of decibels, as a ratio to the quietest sound we are capable of hearing
  Humans perceive sounds over the entire range of 120dB, the upper limit of which will be painful to humans
音量 | 相当于
0 dB | 听力的阈值
60 dB | 日常对话
70 dB | 嘈杂的餐馆
80 dB | 嘈杂的交通，工厂噪音，吸尘器
90 dB | 地铁列车，割草机
100 dB | 电锯，冲击钻
120 dB | 不舒服的阈值（摇滚音乐会，打雷）
140 dB | 痛苦的阈值
160 dB | 伤及鼓膜

## Slide 15: Signal to Noise Ratio (SNR)
Signal to Quantization Noise Ratio (SQNR)
  Aside from any noise that may have been present in the original analog signal, there is also an additional error that results from quantization.
  It is called quantization noise (or quantization error).
  Linear quantization : samples are typically stored as uniformly quantized values.
  Non-uniform quantization: set up more finely-spaced levels where humans hear with the most acuity.-law and A-law encoding.

## Slide 16: Signal to Noise Ratio (SNR)
思考题
  信号的电压为100V，噪声的电压为10V，求SNR为？
  a. 10dB
  b. 20dB
  c. 40dB

## Slide 17: Outline of Lecture 05
Digitization of Sound
  Sound and Digitization
  Nyquist Theorem
  Signal to Noise Ratio (SNR)
Quantization and Transmission of Audio
Experiments

## Slide 18: Quantization and Transmission of Audio
Coding of Audio
  Quantization and transformation of data are collectively known as coding of the data.
    Differences in signals between the present and a past time can reduce the size of signal values and also concentrate the histogram of pixel values (differences, now) into a much smaller range.
  In general, producing quantized sampled output for audio is called PCM (Pulse Code Modulation). The differences version is called DPCM (and a crude but efficient variant is called DM). The adaptive version is called ADPCM.

## Slide 19: Quantization and Transmission of Audio
Pulse Code Modulation in Speech Compression
Pulse Code Modulation (PCM).
(a) Original analog signal
and its corresponding PCM signals.
(b) Decoded staircase signal. (c) Reconstructed signal after low-pass filtering.

## Slide 20: Quantization and Transmission of Audio
PCM in Speech Compression
  The complete scheme for encoding and decoding telephony signals is shown as a schematic in Figure below.
PCM signal encoding and decoding

## Slide 21: Quantization and Transmission of Audio
Lossless Predictive Coding
  Predictive coding: simply means transmitting differences -- predict the next sample as being equal to the current sample; send not the sample itself but the difference between previous and next.
  Predictive coding consists of finding differences, and transmitting these using a PCM system.
  Note that differences of integers will be integers.
  Input signal:
  Predict values:
  Error:
  c) Some function of a few of the previous values provides a better prediction.

## Slide 22: Quantization and Transmission of Audio
Lossless Predictive Coding
  The idea of forming differences is to make the histogram of sample values more peaked.
  Coding scheme: assigns short codewords to frequently occurring symbols.
Differencing concentrates the histogram.
(a): Digital speech signal.
(b): Histogram of digital speech signal values.
(c): Histogram of digital speech signal differences.

## Slide 23: Quantization and Transmission of Audio
Lossless Predictive Coding
  Simple example: the sequence , , , , = 21, 22, 27, 25, 22.
The error does center around zero, we see, and coding will be efficient.

## Slide 24: Quantization and Transmission of Audio
Lossless Predictive Coding
  Simple example: the sequence , , , , = 21, 22, 27, 25, 22.
Schematic diagram for Predictive Coding encoder and decoder.

## Slide 25: Quantization and Transmission of Audio
DPCM
  Differential PCM is exactly the same as Predictive Coding, except that it incorporates a quantizer step.
  Our nomenclature: signal values: - the original signal, - the predicted signal, and - the reconstructed signal; Error values: - an error by subtracting the prediction from the actual signal, - an error for quantizing the original error.
  codewords for quantized error values are produced using entropy coding, e.g. Huffman coding (Chapter 7).

## Slide 26: Quantization and Transmission of Audio
DPCM
  Schematic diagram for DPCM:
  Notice that the quantization noise, , is equal to the quantization effect on the error term, .

## Slide 27: Quantization and Transmission of Audio
DPCM
  For example, suppose we adopt the particular predictor below:
  so that is an integer. As well, use the quantization scheme:
  First, we note that the error is in the range −255::255, i.e., there are 511 possible levels for the error term. The quantizer simply divides the error range into 32 patches of about 16 levels each. It also makes the representative reconstructed value for each patch equal to the midway point for each group of 16 levels.

## Slide 28: Quantization and Transmission of Audio
DPCM
  Table below gives output values for any of the input codes

## Slide 29: Quantization and Transmission of Audio
DPCM
  As an example stream of signal values, consider the set of values:
  Prepend extra values f = 130 to replicate the first value, f1. Initialize with quantized error = 0, so that the first reconstructed value is exact:= 130. Then the rest of the values calculated are as follows (with prepended values in a box):

## Slide 30: Quantization and Transmission of Audio
DM
  DM (Delta Modulation): simplified version of DPCM. Often used as a quick AD converter.
  Uniform-Delta DM: use only a single quantized error value, either positive or negative.
  a 1-bit coder. Produces coded output that follows the original signal in a staircase fashion. The set of equations is:
  Note that the prediction simply involves a delay.

## Slide 31: Quantization and Transmission of Audio
DM
  Consider actual numbers: Suppose signal values are
  Define ne an exact reconstructed value = =10.
  use step value k = 4:
  The reconstructed set of values 10, 14, 10, 14 is close to the correct set 10, 11, 13, 15.
  However, DM copes less well with rapidly changing signals. One approach to mitigating this problem is to simply increase the sampling, perhaps to many times the Nyquist rate.

## Slide 32: Outline of Lecture 05
Digitization of Sound
  Sound and Digitization
  Nyquist Theorem
  Signal to Noise Ratio (SNR)
Quantization and Transmission of Audio
Experiments